## Slide 1: “KiCAD for Robots” – A Tutorial
Presented by
Doug Paradis
Copyright © Doug Paradis
Download KiCad: https://www.kicad.org/download/

## Slide 2: What are we going to cover?
There are four parts to the presentation:
  Intro to KiCad’s interface
  How to build a schematic
  How to layout a PCB
  How to get a PCB built at JLCLPCB
Our example PCB will be a “Module Motherboard”.
Small cheap easy to use electronic modules exist for most functions used on a robot.
Wiring many modules together without a PCB can turn into an unreliable “rat’s nest”.
The techniques learned can be used on any PCB.

## Slide 3: KiCad Opening Screen
The Heart
of KiCad
Some things
worth installing
Select the “Plugin and Content Manager”.
Install the “Freerouting” and “Git” plugins.

## Slide 4: New Project
Create a “KiCad_Projects” and a sub-directory for your project.
In the project directory create 3 sub-directories
  Project
  Symbols
  Footprints
  3D-models
In KiCad, File>New Project.
Steer to your directory tree and enter project name. We are using “Secret_Robot_Project”.
Hit Enter and you should see the screen to the Right.
.kicad_pro -> project file
.kicad_pcb -> PCB layout file
.kicad_sch -> Schematic file

## Slide 5: New Project
Click on the Schematic Editor icon or the .kicad_sch file icon.
The screen to the right appears.
This is the Schematic Screen.
The center is the schematic sheet (like it was in paper times…).
The lower right corner has the sheet ‘s title block.
Title block

## Slide 6: Editing the Title Block
Click on the file name field in the Title Block.
In the Page Setting window edit the fields, as you desire.
You can also use File>Page Settings.
You should change the page size from A3 to US letter.
1
2

## Slide 7: New Project
The right menu has what you need to make a schematic.
About halfway down you have the “labels”. They vary in scope depending on the type.
  Global labels connect globally.
  Net labels only connect on the same sheet.
  Hierarchical labels connect within sheet borders and to hierarchical sheet boxes.
In this session, we will not cover hierarchical sheets, but to show a schematic made with them.
Below the shown icons are some icons that deal with drawing shapes on the schematic sheet.
<- select item - IMPORTANT
<- highlight nets
<- add symbol - IMPORTANT
<- add Power sym - IMPORTANT
<- add wire - IMPORTANT
<- add bus
<- add wire to bus
<- add “no connect” flg - IMPORTANT
<- add junction
<- add net label - IMPORTANT
<- add net class directive-IMPORTANT
<- add global label - IMPORTANT
<- add hierarchical label – important but…
<- add sheet (hierarchical) – important but…
<- add sheet pin (hierarchical) –
<- add text – nice for adding comments

## Slide 8: What is a “Symbol”
A symbol is a diagram that is a representation of the part and its pinout. It is a schematic “symbol”.
Examples:
Transistor (NPN)
Resistor
Capacitor
Custom Module
Microprocessor
Module
Either you make your own or you find the module symbol on the internet.

## Slide 9: Custom Symbols
We want to use a TB6612FNA Dual Motor Driver. It doesn’t have a symbol in KiCad. We need to make one.

## Slide 10: KiCAD Library Component Builder
http://kicad.rohrbacher.net/quicklib.php
2
3
4
1
The other settings can usually use the default values.

## Slide 11: KiCAD Library Component Builder
2
3
4
1
When you download the symbol, make sure to click on “keep”.

## Slide 12: Saving the Symbol We Made
Chrome will not automatically download a file form a non-https website. You have to click on the Keep.
What happened?

## Slide 13: Setting Symbol Pin Type
What are electrical types used for?
The electrical type is used by the electrical rule check (ERC) to determine if you made an obvious mistake. ERC is high, limited. All it does is read all electrical types of pins connected to a particular net and check their combination against the error matrix.
Example: By high, connecting two output pins together will result in an error. (Makes sense as one output can be high, and one can be low resulting in a short circuit between the positive supply and ground.
Author: Rene Posch – Aug 2020
Pin Types:
  Input
  Output
  Bidir
  Tri-state
  Passive
  Unspecified
  Power Input
  Power Output
  Open Collector
  Open Emitter
For some details - https://forum.kicad.info/t/electrical-type-of-schematic-symbol-pins-kicad-4-and-kicad-5/9439

## Slide 14: Setting Symbol Pin Type
To make ERC as useful as possible one needs to take care which electrical types to assign to pins.
The datasheet of your component is a good start for this.
From the TB6612FNG datasheet

## Slide 15: Setting Symbol Pin Type
To make ERC as useful as possible one needs to take care which electrical types to assign to pins. The datasheet of your component is a good start for this.
Pins through which your component is supplied (vcc, gnd, vss, …) are power inputs.
Digital and analog input pins are inputs.
Digital and analog output pins are output (For digital pins, use this only if the pin is push and pull capable or has an internal pull-up or pull-down network.)
  output pins can not be connected to other output pins or bidirectional (avoiding of possible short circuit)
Certain bus pins (SDA of i2c) , … are bidirectional
  Any pin that can be in both input or output state depending on current system state.
Pins for passive devices and pins that are always only connected to other passive devices are passive
Pins that are intended to supply power to other devices use power output (output pin of a dc/dc converter, a voltage regulator, …)
  multiple power output pins can not be connected (avoiding of power supply short)
“Not connected” is used for all pins of the footprint that have no function in the symbol. (You can make them invisible to reduce clutter but don’t stack them. open-source they will open-source each other.)
  NC pins can still be connected in kicad but there will be an error in ERC. Note that stacked NC pins are connected.
Open collector is used for open collector or open drain outputs (output pins that need an external pull up)
Open emitter are used for open emitter or open source outputs (output pins that need an external pull down)
Tri-state is used for output pins that have a high impedance state (high Z) Such pins have the following possible states.
  High -> low impedance connection to high signal voltage (in most cases the positive supply voltage)
  Low -> low impedance connection to low signal voltage (in most case GND)
  High Z -> no connection to anything. (high impedance state)
Pins who can be both input or output depending on configuration (a typical GPIO pin) can be either marked as bidirectional or unspecified.
Author: Rene Posch – Aug 2020
https://forum.kicad.info/t/electrical-type-of-schematic-symbol-pins-kicad-4-and-kicad-5/9439
For Reference.
Worry about later.

## Slide 16: Adding the Symbol to Our Project’s Symbol Library
Symbol Editor
File>New Library
Select Project
Click Ok
2
1
3

## Slide 17: Adding the Symbol to Our Project’s Symbol Library
Symbol Editor
Navigate to project directory
Name Library
Click Save
1
2
3
Back in the Symbol Editor
Use Search to find New Library
Click dropdown
Library will be empty
2
1
3

## Slide 18: Adding the Symbol to Our Project’s Symbol Library
In the Symbol Editor File>Import>Symbol
Hit Enter
1
3
Navigate to your symbols sub-directory
Select the symbol library we made
Click Open
1
2
3

## Slide 19: Saving the Symbol We Made
In the Symbol Editor, the symbol should show up in our project library.
Click Save icon.
1
2
Symbol Saved

## Slide 20: Finally! – Using the Symbol, We Made
On the schematic sheet, select the Add Symbol icon.
Click in the sheet.

## Slide 21: Finally! – Using the Symbol, We Made
On the Choose Symbol window, search for our Library and Symbol.
Select symbol.
Place symbol on schematic sheet. The symbol will be placed where you click.
1
2
3

## Slide 22: Symbol Exercise
Place the following symbols on your schematic sheet.
LED
R_US (resistor using US style symbol)
Screw_terminal_01x02
Conn_01x04
Conn_01x03_Pin
Jumper_2_Open
TestPoint
C (non-polarized capacitor)
GND
+3.3V
PWR_FLAG
Use the “Add Power” Icon (below the “Add Symbol”).

## Slide 23: Downloading Some Resources…
Go to http:// <link to resources> and download the zip file and unzip it.
Open the project file

## Slide 24: The New Schematic
Find the ERC icon and run ERC.
You should see two warnings and one error.
Warnings are marked with a yellow arrow and errors are marked with a red arrow.
Fix one warning and the error.
The new project symbol library is “Presentation_Proj_Library”.

## Slide 25: Exercise Solution…
The two warnings are:
A modified instance of a connector. This one was done on purpose and is of little consequence.
An extra “not-connected” symbol in the C-4 area of the sheet. This is a common extra mouse click type of error. This symbol should be removed.
The error is a missing PWR_FLAG on the “Bminus” trace, which goes to the V-IN pins to both voltage regulators (GND).

## Slide 26: PWR_FLAGs
PWR_FLAGs are used by KiCad as a way to tell the ERC that power nets are connected to a power source when there is no explicit power source.
The most common situation is an external battery being connected to a voltage regulator through a connector.
Power Input type pins must be connected to a Power Output type pin. The pins on a connector are Passive.
PWR_FLAG symbol is found in the Add Power symbols.

## Slide 27: Net Classes
Q: What is a “net” vs. a “trace”?
A: A "net" is not the same as a "trace," but rather a "net" represents a group of connected components on a circuit board, while a "trace" is the physical copper line on the PCB that connects those components within a specific net; essentially, a net is the logical connection, and a trace is the physical manifestation of that connection on the PCB.
For example, A net consisting of +3.3V would be all the connections of +3.3V, where a connection between the +3.3V regulator and a sensor would be a trace.

## Slide 28: Net Classes
Q: What if I want different traces to be different design rules?
A: Netclasses
Net Classes are groups of nets that can be assigned design rules (for the PCB) and graphical properties (for the schematic). In KiCad, each net is part of exactly one net class. If you do not add a net to a specific class, it will be part of the Default class, which always exists.

## Slide 29: Trace Width vs. Current
We need to add a few netclasses:
Battery traces (PCB and Mtr Controller)
Motor power outputs
3.3V and 5V
GND
3
2,4
All nets start in the default netclass, which has a minimum trace width of 10mils or 0.25mm.
You should also consider minimum spaces also.
1

## Slide 30: Setting Up New Net Classes
Schematic Graphical Properties
Also, some other things…
You can adjust the following for Netclasses:
Line Thickness on the schematic sheet.
The color of the net (wires) in the Netclass. 3.3V and 5V.

## Slide 31: Setting Up New Net Classes
PCB Design Rules
You can adjust a Netclass’s:
Clearance and Track Width
Via Size and Hole Size
Micro Via Size and Hole Size
Differential Pair (DP) Width and Gap

## Slide 32: How to Put Nets into Net Classes…
After you setup your Net Classes, you can assign nets to them.
First Way – Add Net Class Directive Labels
Right-side Menu

## Slide 33: How to Put Nets into Net Classes…
Second Way – Click on Net and add Net Class Field
1
2
3
Select Net
Add Field
Select Net Class

## Slide 34: How to Put Nets into Net Classes…
Third Way – Use the Schematic or PCB setup window
1
2
3
Use dropdown
to select Net Class
Must be a wildcarded pattern.
Individual traces need pattern like /x*
Nets don’t need the /
4
Select
Enter pattern

## Slide 35: How to Put Nets into Net Classes…
Fourth Way – For Special Cases, Use Custom Rules in the PCB setup window
1
2
3
These rules allow for the trace “Bminus” of net class GND to have different width and
space than the rest of the net class.

## Slide 36: Before Starting…
It is a good idea to gather all the parts you are going to use.
It makes it easier later when we start to select footprints.

## Slide 37: Final Schematic Sheet

## Slide 38: Footprints
Before you can layout a PCB, you need to have footprints for every part.

## Slide 39: Footprint Assignment Tool
1
When opening the Footprint Assignment Tool
You might see some error boxes. Just click “yes” and OK.
Footprint Assignment tool
Asking if you want to update footprint formats (KiCad is always evolving)
Essentially says that KiCad can’t find footprints.
2
3

## Slide 40: Assigning a Footprint
Available
Footprints
Parts in Schematic
Helpful Filters
Filter Results
1
2
Select part
Select footprint
Click OK
3

## Slide 41: Missing Footprints…
We are lucky because our board has mostly standard parts
Like connectors, resistors, LEDs, and capacitors.
The modules we are using will require finding or building a footprint in the Footprint Editor. Luckily, we found everything.
Since our modules are 2.54mm spaced pins, and we can build our footprints using connectors.

## Slide 42: Footprint Assignment Exercise
Assign a footprint for C1 through C6 (all the same) and R1 through R4 (all the same).
Capacitor details: THT, 2 lead, pitch is 5mm, diameter is 4.7, and the width is 2.5mm.
Resistor details: THT, 2 lead, pitch between leads is 10.1mm, the body diameter is 2.5mm, and the body length is 6.3mm.

## Slide 43: Exercise Answers
C1 through C6: Capacitor_THT:C_Disc_D4.7mm_W2.5mm_P5.00mm
R1 through R4.
Resistor_THT:R_Axial_DIN0207_L6.3mm_D2.5mm_P10.16mm_Horizontal

## Slide 44: Footprint Editor
Existing
Footprints
Add pad
Drawing
Tools
PCB Layers

## Slide 45: Creating a Project Footprint Library
Select Footprint Editor in PCB Editor
Make a new library
Make the library a project library
Name and Save the library in your project
Search for the library to make sure it is created. It will be empty.
3
2
4
5
1

## Slide 46: Adding a Footprint to Your Library
Select Footprint Editor in PCB Editor
Import Footprint
Select file with Footprint (hit open)
Footprint will show up in the Preview pane
Save
1
2
3
4
5

## Slide 47: Adding a Footprint to Your Library
6. Search for and select library
7. Click Ok
8. Check that Footprint shows up in library
6
8
7
ESP32_devkit_v1 sym and ftprint: https://forum.kicad.info/t/esp32-dev-ch340-c-symbol-and-footprint/56483/13
TB6612 module ftprint : https://www.snapeda.com/parts/ROB-14450/SparkFun/view-part/?welcome=home
The ESP32 module had pin
labeling issues.

## Slide 48: All the Footprints Added

## Slide 49: Finally, the PCB Editor
Update PCB from Schematic

## Slide 50: PCB Editor Tools
The right menu has what you need to make a PCB.
<- select item - IMPORTANT
<- local Ratsnest
<- add footprint - IMPORTANT
<- route tracks - IMPORTANT
<- tune length of single track
<- add vias - IMPORTANT
<- add filled zone - IMPORTANT
<- add Rule area
<- add dimensions
<- add text
Drawing Tools tools
<- front copper
<- backside copper
<- front silkscreen
<- backside silkscreen
<- edge cuts (PCB board shape)
<- deletion tool
<- interactively measure
<- set grid origin or drill/place orgin
<- add textbox

## Slide 51: PCB Editor
The top menu has tools that you will also need.
Addins
Scripting
Console
Switch to Schematic
Editor
Design Rule
Checker
Update PCB from Schematic
3D
Viewer
Footprint
Library
Footprint
Editor
The next step

## Slide 52: Reflection on What We Have Done
Completed the schematic, by making the design, adding/making the symbols, and completed the wiring.
Assigned net classes to and passed ERC.
Assigned footprints to all the schematic’s parts.
Placing the footprints and the ratsnest on the PCB and arranging the footprints in a logical order.
Route the wiring. We will use an auto-router.
Print a copy of the final PCB and hand place the parts on it to make sure that everything looks good.
Send the finished PCB design to a PCB manufacturer.
REMAINING:

## Slide 53: Updating the PCB from the Schematic
This places all the part on the PC Editor and connects them with the “ratsnest” which represents the wiring.
Next step is to rearrange the footprints:
There should be a drop sensor in each corner.
The antenna of the ESP32 needs to hang over the edge of the board.
The distance sensors should be near the front of the board.
The motor driver should be on the edge to connect to the terminal blocks. Same with the battery terminal block and voltage regulators.

## Slide 54: First Shot

## Slide 55: Auto Routing
Freerouting is a very nice and fast auto-router.
I prefer to unclick the “restrict pin exit directions”
In the Routing Settings.
You need to add a board
Border before running
Freerouting.
Freerouting

## Slide 56: Board boundaries
KiCad is not very good in detailed graphics, and when board outlines become really complex, they should be drawn in an external program and imported into KiCad.
I prefer to use Inkscape to draw my board boundaries. Some resources:
KiCad - Creating a PCB to exact dimensions,
https://www.youtube.com/watch?v=wzvZ9Ssn0eo
KiCAD - Complex Edge Cuts in KiCAD 5.x with Inkscape
https://www.youtube.com/watch?v=rhqlP8CRct0

## Slide 57: Fill Zones
Using File>Board Setup in the PCB Editor, select “Copper to edge clearance” under Design Rules >Constraints.
Change value to 1.0mm.

## Slide 58: Fill Zones
Fill Zone
Tool
Draw zone around the entire board.

## Slide 59: Fill Zones
Select a Cu Layer.
Select a net to fill the zone.
Click OK.
2
1
3

## Slide 60: Fill Zones
Press “b” to refill zones.
Repeat for backside Cu.
Use net 3.3V.
Use ctrl b to unfill.

## Slide 61: Fill Zones – Completed
Front Cu Layer
Backside Cu Layer

## Slide 62: Run ERC – before making Gerber files
ERC will tell what errors you have in your PCB placements.
Generally, the errors are can be easily fixed.
Look at the warnings, but usually they can be ignored.

## Slide 63: Producing the Gerber Files
For JLCPCB use the instructions from this link:
https://jlcpcb.com/help/article/how-to-generate-gerber-and-drill-files-in-kicad-8
After making the Gerber, drill, and drill map files, it is a good idea to use a 3rd party Gerber viewer. JLCPCB recommends their own JLCPCB Gerber Viewer or open-source Gerbv.
JLCPCB Gerber Viewer: https://jlcpcb.com/RGE
Gerbv download: https://gerbv.github.io/

## Slide 66: All Robots Start with An Idea – A Tabletop Robot
Parts:
  2 yellow TTmotor motors from DFRobot with quadrature encoders
  ESP32-WROOM-32 devkit v1 (30 pin version) module
  4 IR drop sensors – HiLetgo TCRT5000 IR sensors (GPIO)
  Dual H bridge for motors – ZK-5AD module (GPIO) or TB6612FNG (GPIO)
  9 DOF IMU – BNO085 (I2C/UART)
  7.2V to 5V regulator - 5V version of Mini360 buck converter (Pwr)
  7.2V to 3.3V regulator – 3.3V version of Mini360 buck converter (Pwr)
  Distance sensor – either a HSR04 ultrasonic (GPIO) or a TFMini-S ToF LiDAR (UART/I2C)
  Power and Start switches, “on” LED with current limiting resistor
  Bumper (optional – should have provisions for)
P




= on PCB - other parts will have headers on PCB.

## Slide 67: Parts - ESP32 DevKit v1
There is an additional UART – you have to assign the pins.
2-2.54mm-15p
headers

## Slide 68: Parts - other
Ideally, we will have polarized headers for all the parts on our PCB.
BNO085
ZK-5AD Mtr controller
Pwr and Start Switches
IR Drop Sensors (4x)
DFRobot TTMotor w/
Encoder
Mini360 Vreg (1 or 2x)
TFMini-S
Seeed Studio
Ultrasonic Ranger (upgraded HC-SR04)
2.54mm-10p
To XH-4p
2.54mm-6p
Grove 2.0mm-4p
XH - 3p or 4p
(2.54mm)
XH-2p (2.54MM)
GH1.25-4P
PH2.0-4P
For Encoders
4 – 1p
headers
Adifruit
Knock Off